## Slide 1: Virtual Memory, Address-Translation and Paging
INF-2201 Operating Systems – Spring 2019
Lars Ailo Bongo (larsab@cs.uit.no)
… based on presentations created by
Lars Ailo Bongo, Tore Brox-Larsen, Bård Fjukstad, Daniel Stødle, Otto Anshus, Thomas Plagemann, Kai Li, Andy Bavier
Tanenbaum & Bo,Modern Operating Systems:4th ed.

## Slide 2: Overview
Part 1
  Virtual Memory
    Virtualization
    Protection
  Address Translation
    Base and bound
    Segmentation
    Paging
    Translation look-ahead buffer
Part 2: Paging and replacement
Part 3: Design Issues

## Slide 3: Latency Numbers Every Programmer Should Know
https://people.eecs.berkeley.edu/~rcs/research/interactive_latency.html

## Slide 4: The Big Picture
DRAM is fast, but relatively expensive
  $25/GB
  20-30ns latency
  10-80GB’s/sec
Disk is inexpensive, but slow
  $0.2-1/GB (100 less expensive)
  5-10ms latency (100K times slower)
  40-80MB/sec per disk (1,000 times less)
Our goals
  Run programs as efficiently as possible
  Make the system as safe as possible

## Slide 5: Issues
Many processes
  The more processes a system can handle, the better
Address space size
  Many small processes whose total size may exceed memory
  Even one process may exceed the physical memory size
Protection
  A user process should not crash the system
  A user process should not do bad things to other processes

## Slide 6: No Memory Abstraction
Figure 3-1. Three simple ways of organizing memory with an operating system and one user process. Other possibilities also exist
Tanenbaum & Bo,Modern Operating Systems:4th ed., (c) 2013 Prentice-Hall, Inc. All rights reserved.

## Slide 7: A Simple System
Only physical memory
  Applications use physical memory directly
Run three processes
  emacs, pine, gcc
What if
  gcc has an address error?
  emacs writes at x7050?
  pine needs to expand?
  emacs needs more memory than is on the machine?

## Slide 8: Protection Issues
Errors in one process should not affect others
For each process, check each load and store instruction to allow only legal memory references

## Slide 9: Expansion or Transparency Issue
A process should be able to run regardless of its physical location or the physical memory size
Give each process a large, static “fake” address space
As a process runs, relocate each load and store to its actual memory

## Slide 10: Virtual Memory
Flexible
  Processes can move in memory as they execute, partially in memory and partially on disk
Simple
  Make applications very simple in terms of memory accesses
Efficient
  20/80 rule: 20% of memory gets 80% of references
  Keep the 20% in physical memory
Design issues
  How is protection enforced?
  How are processes relocated?
  How is memory partitioned?

## Slide 11: Address Mapping and Granularity
Must have some “mapping” mechanism
  Virtual addresses map to DRAM physical addresses or disk addresses
Mapping must have some granularity
  Granularity determines flexibility
  Finer granularity requires more mapping information
Extremes
  Any byte to any byte: mapping equals program size
  Map whole segments: larger segments problematic

## Slide 12: Generic Address Translation
Memory Management Unit (MMU) translates virtual address into physical address for each load and store
Software (privileged) controls the translation
CPU view
  Virtual addresses
Each process has its own memory space [0, high]
  Address space
Memory or I/O device view
  Physical addresses

## Slide 13: Goals of Translation
Implicit translation for each memory reference
A hit should be very fast
Trigger an exception on a miss
Protected from user’s faults

## Slide 14: Base and Bound
Built in Cray-1
Each process has a pair (base, bound)
Protection
  A process can only access physical memory in [base, base+bound]
On a context switch
  Save/restore base, bound registers
Pros
  Relocation possible
  Simple
  Flat and no paging
Cons
  Fragmentation
  Hard to share
  Difficult to use disks

## Slide 15: Segmentation
Each process has a table of (seg, size)
Treats (seg, size) as a fine-grained (base, bound)
Protection
  Each entry has (nil, read, write, exec)
On a context switch
  Save/restore the table and a pointer to the table in kernel memory
Pros
  Efficient
  Easy to share
Cons
  Segments must be contiguous in physical memory
  Fragmentation within a segment
  Complex management

## Slide 16: Segmentation: Example Systems
Burroughs B5000
General Electrix GE-645 (Multics)
  www.multicians.org
Intel iAPX 432
IBM AS/400
X86 (limited)
Notes: Burroughs B5000, GE-645, iAPX 432 and AS/400 are all examples of computer architectures that strive for some “higher-level” functionality.
B5000 Language (Algol) oriented architecture. Stack instruction set architecture
GE-645 Segments are a central quality, Supports Multics (see multicians.org). Ge later became Honeywell-Bull and Bull. Bull was a French computer manufacturer named after Norwegian computing pioneer and industrialist Bull.
iAPX 432 was Intels design for a 32 bit architecture breaking away from the x86-heritance. It was designed to support objects and capabilities, object oriented languages, garbage collection and other features. In Oslo iAPX 432 was referred to as a Simula-processor, whereas in the rest of the world it was similarly referred to as an Ada-architecture. This was the first time Intel tried to break away from the x86 legacy. The design was not commercially successful. Instead Intel survived on the backwards compatible, and novel, 386 architecture. A much less prestigious, possibly “undercover” project at Intel
AS/400 was a continuation of the previously System/38, a capability-based processor.
B5000, iAPX 432, and AS/400 are all describes in Steven M. Levy’s book on Capability-based computer systems.

## Slide 17: Paging
Use a fixed size unit called page instead of segment
Use a page table to translate
  “Principle: Introducing (one level of) indirection”
Various bits in each entry
Context switch
  Similar to segmentation
What should page size be?
Pros
  Simple allocation
  Easy to share
Cons
  Big table
  How to deal with holes?
Notes: “Swapping” (by the OS) and “Overlays” (by the application) were techniques that predates paging.
Segmentation (without paging) also predates Paging and segmentation with paging.

## Slide 18: Paging (1)
Figure 3-8. The position and function of the MMU. Here the MMU is shown as being a part of the CPU chip because it commonly is nowadays. However, logically it could be a separate chip and was years ago.
Tanenbaum & Bo,Modern Operating Systems:4th ed., (c) 2013 Prentice-Hall, Inc. All rights reserved.

## Slide 19: Paging (2)
Figure 3-9. The relation between virtual addresses and physical memory addresses is given by the page table. Every page begins on a multiple of 4096 and ends 4095 addresses higher, so 4K–8K really means 4096–8191 and 8K to 12K means 8192–12287
Tanenbaum & Bo,Modern Operating Systems:4th ed., (c) 2013 Prentice-Hall, Inc. All rights reserved.

## Slide 20: Paging (3)
Figure 3-10. The internal operation of the MMU with 16 4-KB pages.
Tanenbaum & Bo,Modern Operating Systems:4th ed., (c) 2013 Prentice-Hall, Inc. All rights reserved.

## Slide 21: Structure of a Page Table Entry
Figure 3-11. A typical page table entry.
Tanenbaum & Bo,Modern Operating Systems:4th ed., (c) 2013 Prentice-Hall, Inc. All rights reserved.

## Slide 22: Speeding Up Paging
Major issues faced:
The mapping from virtual address to physical address must be fast.
If the virtual address space is large, the page table will be large.
Tanenbaum & Bo,Modern Operating Systems:4th ed., (c) 2013 Prentice-Hall, Inc. All rights reserved.

## Slide 23: How Many PTEs Do We Need?
Assume 4KB page
  Equals “low order” 12 bits
Worst case for 32-bit address machine
  # of processes × 220
  220 PTEs per page table (~4Mbytes), but there might be 10K processes. They won’t fit in memory together
What about 64-bit address machine?
  # of processes × 252
  A page table cannot fit in a disk (252 PTEs = 16PBytes)!

## Slide 24: Segmentation with Paging

## Slide 25: Multiple-Level Page Tables

## Slide 26: Inverted Page Tables
Main idea
  One PTE for each physical page frame
  Hash (Vpage, pid) to Ppage#
Pros
  Small page table for large address space
Cons
  Potential for poor cache performance
  Lookup is difficult
  Overhead of managing hash chains, etc

## Slide 27: Virtual-To-Physical Lookups
Programs only know virtual addresses
  Each program or process starts from 0 to high address
Each virtual address must be translated
  May involve walking through the hierarchical page table
  Since the page table stored in memory, a program memory access may requires several actual memory accesses
Solution
  Cache “active” part of page table in a very fast memory

## Slide 28: Virtual Page Lookup
From: http://www.pearsonhighered.com/samplechapter/0130610143.pdf

## Slide 29: Translation Look-aside Buffer (TLB)
Notes: Indirection through the page table by itself means that you need one (or more) extra memory accesses to get to the desired memory location. The basic idea of the TLB is to provide a cache for page-table mappings.
gRemember most programs tends to make a large number of references to a small number of pages.
TLB is a hardware feature. All lookups are done in parallel, requires specialized hardware.
Access is also checked against protection bits.
A miss is fast, a few ns if page is in memory but not in TLB.

## Slide 30: Bits in a TLB Entry
Common (necessary) bits
  Virtual page number: match with the virtual address
  Physical page number: translated address
  Valid
  Access bits: kernel and user (nil, read, write)
Optional (useful) bits
  Process tag
  Reference
  Modify
  Cacheable

## Slide 31: Hardware-Controlled TLB
On a TLB miss
  Hardware loads the PTE into the TLB
    Write back and replace an entry if there is no free entry
  Generate a fault if the page containing the PTE is invalid
  VM software performs fault handling
  Restart the CPU
On a TLB hit, hardware checks the valid bit
  If valid, pointer to page frame in memory
  If invalid, the hardware generates a page fault
    Perform page fault handling
    Restart the faulting instruction

## Slide 32: Software-Controlled TLB
On a miss in TLB
  Write back if there is no free entry
  Check if the page containing the PTE is in memory
  If not, perform page fault handling
  Load the PTE into the TLB
  Restart the faulting instruction
On a hit in TLB, the hardware checks valid bit
  If valid, pointer to page frame in memory
  If invalid, the hardware generates a page fault
    Perform page fault handling
    Restart the faulting instruction

## Slide 33: Hardware vs. Software Controlled
Hardware approach
  Efficient
  Inflexible
  Need more space for page table
Software approach
  Flexible
  Software can do mappings by hashing
    PP# → (Pid, VP#)
    (Pid, VP#) → PP#
  Can deal with large virtual address space

## Slide 34: Caches and TLBs
Both may be single- or multiple level
Both may be unified or split
Both may offer different levels of associativit

## Slide 35: Cache vs. TLB
Notes: Both types may be single- or multiple level, unified or split into separate I and D. If the replacement policy is free to choose any entry in the cache to hold the copy, the cache is called fully associative. At the other extreme, if each entry in main memory can go in just one place in the cache, the cache is direct mapped. Many caches implement a compromise in which each entry in main memory can go to any one of N places in the cache, and are described as N-way set associative.[7] For example, the level-1 data cache in an AMD Athlon is two-way set associative, which means that any particular location in main memory can be cached in either of two locations in the level-1 data cache.
TLBs tend to offer higher (or full) associativity than instruction-, data-, or unified caches.

## Slide 36: Detour: Accosiativity
http://en.wikipedia.org/wiki/File:Cache,associative-fill-both.png
Notes: If the replacement policy is free to choose any entry in the cache to hold the copy, the cache is called fully associative. At the other extreme, if each entry in main memory can go in just one place in the cache, the cache is direct mapped. Many caches implement a compromise in which each entry in main memory can go to any one of N places in the cache, and are described as N-way set associative.[7] For example, the level-1 data cache in an AMD Athlon is two-way set associative, which means that any particular location in main memory can be cached in either of two locations in the level-1 data cache.

## Slide 37
www.cs.hmc.edu/~geoff/classes/.../class14_vm1.ppt

## Slide 38: TLB Related Issues
What TLB entry to be replaced?
  Random
  Pseudo LRU
What happens on a context switch?
  Process tag: change TLB registers and process register
  No process tag: Invalidate the entire TLB contents
What happens when changing a page table entry?
  Change the entry in memory
  Invalidate the TLB entry

## Slide 39: Consistency Issues
“Snoopy” cache protocols (hardware)
  Maintain consistency with DRAM, even when DMA happens
Consistency between DRAM and TLBs (software)
  You need to flush related TLBs whenever changing a page table entry in memory
TLB “shoot-down”
  On multiprocessors, when you modify a page table entry, you need to flush all related TLB entries on all processors, why?

## Slide 40: Summary – Part 1
Virtual Memory
  Virtualization makes software development easier and enables memory resource utilization better
  Separate address spaces provide protection and isolate faults
Address translation
  Base and bound: very simple but limited
  Segmentation: useful but complex
Paging
  TLB: fast translation for paging
  VM needs to take care of TLB consistency issues