## Slide 1: Storage Systems
Lars Ailo Bongo Inf-2201, University of Tromsø, Spring 2019

## Slide 2: Big Data Sources
Voluntary human produced content
  Videos, photos, audio…
Involuntary produced content
  Online activity logging, tax records…
Scientific instruments
  CERN LHC, Sloan Digital Sky Survey, brain simulations, DNA sequencers…

## Slide 3: Big Data
How big?

## Slide 4: Dataset Size
< 8GB
< 1TB
TBs
PBs

## Slide 5: Dataset Size (NxM)
Billions of samples & few dimensions, or
Billions of samples & thousands of dimensions, or
Thousands of samples & thousands of dimensions

## Slide 6: Data Analysis Framework

## Slide 7: Computation Time
<100ms
seconds
minutes
hours
weeks

## Slide 8: Optimizations
R or Matlab implementation
Algorithm parameter tuning
C++/ Java / … implementation
Data structure optimization
Multi-threaded parallelization (single machine)
Distributed parallelization (multiple-machines)

## Slide 9
Notes: Published in 2009
Jim Gray’s talk 2007
Empirical
Theoretical
Computational
Data exploration

## Slide 10: Data challenges

## Slide 11: Data growth in the life sciences
Data growth at EMBL-EBI
Source: Charles E. Cook et al. Nucl. Acids Res. 2016;44:D20-D26
Notes: Phenomenal data growth – dotted lines represents doubling every twelve months
(A) Data accumulation at EMBL-EBI by data type, for example mass spectrometry (MS); (B) Data accumulation by dedicated resource, for example PRIDE. The y-axis is log-scale, with the slope of the dashed lines indicating a 12-month doubling time. Continued data growth is seen in all types of data at EMBL-EBI and all data resources. In all data resources shown here, growth rates are predicted to continue increasing, with notable sustained exponential growth in PRIDE, the European Genome-phenome Archive (EGA) and MetaboLights: all have doubling times of around 12 months. All three contributing platforms show rates that are increasing over time, with data growing exponentially with around a 12-month doubling time.

## Slide 12: The data challenge: Data growth
Computer speed and storage capacity is doubling every 18 months and this rate is steady
DNA sequence data is doubling every 6-8 months over the last 3 years and looks to continue for this decade
Source: Charles E. Cook at al. Nucl. Acids Res. 2016; 44: D20-D26

## Slide 13: Data resources in life science
Nucleic Acids Research annual Database Issue
and the NAR online Molecular Biology Database Collection in 2012.
MY Galperin, GR Cochrane – Nucleic Acids Research, 2011
~1800
molecular biology
data resources

## Slide 14: We generate data faster than we can deposit it
14
~100 GB
~4 TB
~4 TB
24 hours
100 Mb
~5 hours
~4 days
~4 days
DNA sequencing
Mass spectrometry
Microscopy
Network file transfer rate
Notes: We are generating data faster than we can transfer it.
Even with faster lines we are talking major computational bottlenecks in file transfer.
Technology get cheaper and faster
~15.000 hospital
~4.000 universities
~2.000 life sciences research institutes
How much data we will produce? How we will store it?

## Slide 15: Overview
Magnetic disks
Disk arrays
Flash storage
DRAM storage
Storage hierarchy

## Slide 16: Storage
Reliability
  Archival
  Reliable
  Persistent
  Temporal
Access pattern
  Write or read intensive
  Sequential or random access
  Low-latency or high throughput
Cost
Power

## Slide 17: The Memory Hierarchy
Jiahua He, Arun Jagatheesan, Sandeep Gupta, Jeffrey Bennett, Allan Snavely, "DASH: a Recipe for a Flash-based Data Intensive Supercomputer," sc, pp.1-11, 2010 ACM/IEEE International Conference for High Performance Computing, Networking, Storage and Analysis, 2010

## Slide 18: Disk vs. Flash vs. DRAM
 | Disk | Flash | DRAM
Access time (relative) | 1 | 100-1,000 | 0.000001 (1 / 100,000)
Cost (relative) | 1 | 15-25 | 30-150
Bandwidth (relative) | 1 | 1 | 80
Bandwidth/ GB (relative) | 1 |  | 6,000
Bandwidth/ $ (relative) | 1 |  | 160
Source: Computer Architecture A Quantitative Approach

## Slide 19: Punch Cards

## Slide 20: Magnetophone

## Slide 21: Tape Library
Notes: First used: 1951 in UNIVAC-1
Picture: Spectra T-Finity, with 400PB capacity
Tape: Oracle T10000C: 5TB capacity, 250MB/s uncompressed write ratio
Driver typically compress data: 2x ratio

## Slide 22: Scientific Storage Systems
Source: http://www.usenix.org/events/lisa10/tech/slides/cass.pdf

## Slide 24: Hard Drive Teardown
http://www.youtube.com/watch?v=Wiy_eHdj8kg

## Slide 25: Disk Arm and Head
Disk arm
  A disk arm carries disk heads
Disk head
  Mounted on an actuator
  Read and write on disk surface
Read/write operation
  Disk controller receives a command with <track#, sector#>
  Seek the right cylinder (tracks)
  Wait until the right sector comes
  Perform read/write

## Slide 26: Mechanical Component of A Disk Drive
Tracks
  Concentric rings around disk surface, bits laid out serially along each track
Cylinder
  A track of the platter, 1000-5000 cylinders per zone, 1 spare per zone
Sectors
  Each track is split into arc of track (min unit of transfer)

## Slide 27: A Typical Magnetic Disk Controller
External connection
  Parallel ATA (aka IDE or EIDE), Serial ATA, SCSI, Serial Attached SCSI (SAS), Fibre Channel, FireWire, USB
Cache
  Buffer data between disk and interface
Controller
  Read/write operation
  Cache replacement
  Failure detection and recovery

## Slide 28: Disk Caching
Method
  Use DRAM to cache recently accessed blocks
    Most disks has 32MB
    Some of the RAM space stores “firmware” (an embedded OS)
  Blocks are replaced usually in an LRU order
Pros
  Good for reads if accesses have locality
Cons
  Cost
  Need to deal with reliable writes

## Slide 29: Disk Sectors
Where do they come from?
  Formatting process
  Logical maps to physical
What is a sector?
  Header (ID, defect flag, …)
  Real space (e.g. 512 bytes)
  Trailer (ECC code)
What about errors?
  Detect errors in a sector
  Correct them with ECC
  If not recoverable, replace it with a spare
  Skip bad sectors in the future

## Slide 30: Disks Were Large

## Slide 31: They Are Now Much Smaller
Notes: 3.5” 0.5-3TB
2.5” 320-640

## Slide 32: Areal Density vs. Moore’s Law

## Slide 33: 50 Years Later (Mark Kryder at SNW 2006)

## Slide 34: Sample Disk Specs (from Seagate)
 | Cheetah 15k.7 | Barracuda XT
Capacity |  | 
Formatted capacity (GB) | 600 | 2000
Discs | 4 | 4
Heads | 8 | 8
Sector size (bytes) | 512 | 512
Performance |  | 
External interface | Ultra320 SCSI, FC, S. SCSI | SATA
Spindle speed (RPM) | 15,000 | 7,200
Average latency (msec) | 2 | 4.16
Seek time, read/write (msec) | 3.5/3.9 | 8.5/9.5
Track-to-track read/write (msec) | 0.2-0.4 | 0.8/1.0
Internal transfer (MB/sec) | 1,450-2,370 | 600
Transfer rate (MB/sec) | 122-204 | 138
Cache size (MB) | 16 | 64
Reliability |  | 
Recoverable read errors | 1 per 1012 bits | 1 per 1010 bits
Non-recoverable read errors | 1 per 1016 bits | 1 per 1014 bits

## Slide 35: Disk Performance (2TB disk)
Seek
  Position heads over cylinder, typically 3.5-9.5 ms
Rotational delay
  Wait for a sector to rotate underneath the heads
  Typically 8 - 4 ms (7,200 – 15,000RPM) or . rotation takes 4 - 2ms
Transfer bytes
  Transfer bandwidth is typically 40-138 Mbytes/sec
Performance of transfer 1 Kbytes
  Seek (4 ms) + half rotational delay (2ms) + transfer (0.013 ms)
  Total time is 6.01 ms or 167 Kbytes/sec (1/360 of 60MB/sec)!

## Slide 36: More on Performance
What transfer size can get 90% of the disk bandwidth?
  Assume Disk BW = 60MB/sec, . rotation = 2ms, . seek = 4ms
  BW * 90% = size / (size/BW + rotation + seek) size = BW * (rotation + seek) * 0.9 / 0.1= 60MB * 0.006 * 0.9 / 0.1 = 3.24MB
Seek and rotational times dominate the cost of small accesses
  Disk transfer bandwidth are wasted
  Need algorithms to reduce seek time
Speed depends on which sectors to access
  Are outer tracks or inner tracks faster?
Block Size | % of Disk Transfer Bandwidth
1Kbytes | 0.28%
1Mbytes | 73.99%
3.24Mbytes | 90%

## Slide 37: FIFO (FCFS) order
Method
  First come first serve
Pros
  Fairness among requests
  In the order applications expect
Cons
  Arrival may be on random spots on the disk (long seeks)
  Wild swing can happen

## Slide 38: SSTF (Shortest Seek Time First)
Method
  Pick the one closest on disk
  Rotational delay is in calculation
Pros
  Try to minimize seek time
Cons
  Starvation
Question
  Is SSTF optimal?
  Can we avoid the starvation?

## Slide 39: Elevator (SCAN)
Method
  Take the closest request in the direction of travel
  Real implementations do not go to the end (called LOOK)
Pros
  Bounded time for each request
Cons
  Request at the other end will take a while

## Slide 40: C-SCAN (Circular SCAN)
Method
  Like SCAN
  But, wrap around
  Real implementation doesn’t go to the end (C-LOOK)
Pros
  Uniform service time
Cons
  Do nothing on the return

## Slide 41: Discussions
Which is your favorite?
  FIFO
  SSTF
  SCAN
  C-SCAN
Disk I/O request buffering
  Where would you buffer requests?
  How long would you buffer requests?

## Slide 42: Storage System
Network connected box with many disks
Entry level box has 12 disks
  Mean time to failure?
  How to improve reliability?
  What if there are 1000 disks?

## Slide 43: RAID (Redundant Array of Independent Disks)
Main idea
  Store the error correcting codes on other disks
  General error correcting codes are too powerful
  Use XORs or single parity
  Upon any failure, one can recover the entire block from the spare disk (or any disk) using XORs
Pros
  Reliability
  High bandwidth
Cons
  The controller is complex

## Slide 44: Synopsis of RAID Levels

## Slide 45: RAID Level 6 and Beyond
Goals
  Less computation and fewer updates per random writes
  Small amount of extra disk space
Extended Hamming code
Specialized Eraser Codes
  IBM Even-Odd, NetApp RAID-DP, …
Beyond RAID-6
  Reed-Solomon codes, using MOD 4 equations
  Can be generalized to deal with k (>2) disk failures

## Slide 46
Figure from: Computer Architecture A Quantitative Approach

## Slide 47: An Alternative to RAID
Google File System
  Open source version: Hadoop file system
Distributed file system built on top of Linux FS
  Special purpose for data-intensive computing (MapReduce)
  Not intended to replace Linux FS for ordinary jobs
Run on commodity components (clusters)
  Each node in cluster has storage and computation resources
  High aggregate I/O bandwidth
Large blocks (64MB)
Typically 3x replication for blocks
MapReduce jobs

## Slide 48: Dealing with Disk Failures
What failures
  Power failures
  Disk failures
  Human failures
What mechanisms required
  NVRAM for power failures
  Hot swappable capability
  Monitoring hardware
RAID reconstruction
  Reconstruction during operation
  What happens if a reconstruction fail?
  What happens if the OS crashes during a reconstruction

## Slide 49: Next Generation: FLASH
Flash chip density increases on the Moore’s law curve
  1995 16 Mb NAND flash chips
  2005 16 Gb NAND flash chips
  2009 64 Gb NAND flash chips
  Doubled each year since 1995
Market driven by Phones, Cameras, iPod,… Low entry-cost, ~$30/chip → ~$3/chip
2012 1 Tb NAND flash == 128 Gb chip == 1TB or 2TB “disk” for ~$400 or 128GB disk for $40 or 32GB disk for $5
Samsung prediction
Retail prices as of March 2012:
Biggest SSD: 512 GB ($850)
128GB SSD for $230
(2TB disk about $200)
32GB SD: $90

## Slide 50: NAND Flash Memory
https://www.youtube.com/watch?v=w3uwpuNY-Ww

## Slide 51: Flash Memory
NOR
  Byte addressable
  Often used for BIOS
  Much higher price than for NAND
NAND
  Dominant for consumer and enterprise devices
  Single Level Cell (SLC) vs. Multi Level Cell (MLC):
    SLC is more robust but expensive
    MLC offers higher density and lower price

## Slide 52: NAND Memory Organization
Organized into a set of erase blocks (EB)
Each erase block has a set of pages
Example configuration for a 512 MB NAND device:
  4096 EB’s, 64 pages per EB, 2112 bytes per page (2KB user data + 64 bytes metadata)
Read:
  Random access on any page, multiple times
  25-60s
Write
  Data must be written sequentially to pages in an erase block
  Entire page should be written for best reliability
  250-900 s
Erase:
  Entire erase block must be erased before re-writing
  Up to 3.5ms

## Slide 53: Flash Translation Layer
Emulate a hard disk by exposing an array of blocks
Logic block mapping
  Map from logical to physical blocks
  Cannot do random writes
  Granularity: block vs. page (read-modify-write block vs. large RAM for storing map table
  Hybrid approach often used: maintain a small set of log blocks for page level mapping
Garbage collection
  Maintain an allocation pool of clean blocks (blocks must be erased before reuse)
  Recycle invalidated pages
  Merge blocks if page level mapping
Wear leveling
  Most writes are to a few pages (metadata)
  Even out writes over blocks

## Slide 54: What’s Wrong With FLASH?
Expensive: $/GB
  2x less than cheap DRAM
  50x more than disk today, may drop to 10x in 2012
Limited lifetime
  ~100k to 1M writes / page (single cell)
  ~15k to 1M writes / page (single cell)
  requires “wear leveling” but, if you have 1,000M pages, then 15,000 years to “use” the pages.
Current performance limitations
  Slow to write can only write 0’s, so erase (set all 1) then write
  Large (e.g. 128K) segments to erase

## Slide 55: Current Development
Flash Translation Layer (FTL)
  Remapping
  Wear-leveling
  Write faster
Form factors
  SSD
  USB, SD, Stick,…
  PCI cards
Performance
  Fusion-IO cards achieves 200K IOPS

## Slide 56: Hardware/Software Architecture
SSD
SSD
HD
Controller
Controller
Controller
Block Device Driver
Block Device Driver
I/O Scheduler
Generic Block Layer
File System
File System
Virtual File System
Device Driver
Flash Storage Layer
File System
SATA
PCI-E
HW
SW (OS)

## Slide 57: Discussions
Where to put a flash drive in the storage hierarchy?
Which new algorithms need to be developed?
Should the OS treat flash drive as a hard drive?

## Slide 58: Good Paper
Following figures are from that paper

## Slide 59: SSD Bandwidths (raw I/O)

## Slide 60: Do reads on SSD have uniform latency?
Figure 2

## Slide 61: Would random writes be worst case?
Figure 3

## Slide 62: Is a disk cache effective for SSDs?
Fig. 5

## Slide 63: Do reads and writes interfere with each other?
Fig. 6

## Slide 64: Do background operations affect performance?
Fig. 7

## Slide 65: Would increasing workload randomness degrade performance?
Fig. 8

## Slide 66: Non-volatile DRAM (NVRAM)
Battery backed DRAM
  Backup power during power-out
  Ordinary DRAM technology
One part of a storage system
Expensive
Targeted at specific application domains such as databases
(Netlist Nvvault)

## Slide 67: Remote Direct Memory Access

## Slide 68: Low latency remote memory access

## Slide 69: DRAM Storage Systems
Currently increasing interest in DRAM only storage systems
  All data structures in memory
  Data is backed on disk in background
In-memory databases
  Database entirely in memory
  Often used for analytics
  Business critical data stored on ordinary databases
RAM Cloud
  A big compute cluster
  Data structures replicated over many computers
  Data also written to disk
  http://www.sigops.org/sosp/sosp11/current/2011-Cascais/03-ongaro-online.pdf

## Slide 70: Traditional Data Center Storage Hierarchy
Network
SAN
Clients
Server
Storage
…
Storage
Onsite Backup
Offsite backup
Remote mirror

## Slide 71: Evolved Data Center Storage Hierarchy
Network
Clients
Storage
…
Onsite Backup
Offsite backup
Remote mirror
Network Attached Storage (NAS)
w/ snapshots to protect data

## Slide 72: Modern Data Center Storage Hierarchy
Network
Clients
…
Onsite Backup
Remote mirror
Network Attached Storage (NAS)
w/ snapshots to protect data
WAN
Remote Backup
“Deduplication”
Capacity and bandwidth optimization

## Slide 73: Very Large Dataset Storage Hierarchy
Network
Clients
…
Onsite Backup
Remote mirror
Network Attached Storage (NAS)
w/ snapshots to protect data
WAN
Remote Backup
Distributed Storage w. internal replication

## Slide 74: 10.000 Years Storage Systesm
How to build a storage system with a mean time to failure = 10.000 years?
Fun read
Uses lots of basic storage system principles
I/O performance not great

## Slide 75: Summary
Disk is complex
Disk real density is on Moore’s law curve
Need large disk blocks to achieve good throughput
OS needs to perform disk scheduling
RAID improves reliability and high throughput at a cost
Careful designs to deal with disk failures
Flash memory has emerged at low and high ends
DRAM only storage systems are emerging
Storage hierarchy is complex